## Slide 1: Toward a New Experimental Paradigm for Consumer BCI
Walter Piper
July 2021
Capstone Presentation
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation

## Slide 2: Outline
Context for consumer EEG
Problem Identification and proposed framework
Data Wrangling and Data Engineering
Exploratory Data Analysis
Preprocessing & Modeling
Recommendations & Future Directions
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation

## Slide 3: Brain-Computer Interfaces are having a moment
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Brain Sci. 2021, 11, 43. https://doi.org/10.3390/brainsci11010043 https://www.mdpi.com/journal/brainsci
Notes: Key determinants of brain signal utility:
Spatial : Proximity to neurons / Num Channels
Temporal : Sampling rate
Practical : Cost / Invasive vs. Non-Invasive

## Slide 4: Can non-invasive interfaces also thrive?
Limitations:
Distance from source of signal
Potentially expensive $$$
“Prices for a complete EGI Geodesic configuration range from approximately $30,000–$175,000”
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Notes: Very limited in functionality compared to invasive interfaces.

## Slide 5: Problem Identification
$300 Examples:
Interaxon’s Muse meditation headband (2014)
Neurable’s Enten headphones (2022)
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Challenges:
Few consumer options at affordable price point.
Few channels and noisy data.
Limited use cases, so far.
Strategies:
Market for precise use cases.
Make the most of noisy data.
  Machine Learning
  Supplemental data (ex. gyroscope)

## Slide 6: Consumer-Driven Discovery and Deployment
Exploratory Data Analysis & Feature Engineering
Modeling
Real-Time Deployment
Curiosity & Hypothesis Generation
Self-Experimentation
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Automate as much as possible to make BCI experimentation accessible to others.

## Slide 7: My own hypotheses to test:
I am interested in asynchronous control.
  I would love the ability to mentally recruit my computer to perform an action.
  0. Baseline condition = open eyes
Experimental conditions:
  Test if imagined/mental commands can be distinguished from baseline.
  Test if body-focused attention (body-scan meditation) can be identified.
Positive control (Try to reproduce a known effect):
  Eyes open should be separable from eyes closed. (alpha frequencies ~10Hz)
Additional control condition:
  Test if physical action (repeated button pressing) can be separated from mental action command.
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation

## Slide 8: Muse headband has electrodes over frontal lobe & temporal lobe.
Frontal electrodes
  AF7, AF8
  Low noise.
    Eye-movement artifacts
Temporal (side) electrodes
  TP9, TP10
  High noise
    Muscle tension in jaw and neck.
    Poor fit.
      EEG signal often overwhelmed by muscle activity and heartbeat.
Accelerometer & Gyroscope
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Ground &
Reference Electrodes
AF7
AF8
TP9
TP10
From a neuroscience theory perspective:
Frontal-Temporal coordination is heavily involved in cognitive-emotional integration

## Slide 9: Behavioral experiments can be automated
Exploratory Data Analysis & Feature Engineering
Modeling
Real-Time Deployment
Curiosity & Hypothesis Generation
Self-Experimentation
Allow computer to handle timing and data.
Instructions to human via Text-To-Speech (TTS).
Reduces movement artifacts and improves temporal precision
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation

## Slide 10: Data Pipelines – Data Collection
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Muse EEG headband
Bluetooth
Mind Monitor app
Option 1:
.csv file
Option 2:
OSC network protocol
python-osc
(Multi-threading server mapping message strings to handler functions)
queue.Queue
pyttsx3
(Text-To-Speech instructions during experiment)
pymongo/MongoDB
(Database for long-term storage)
Thread to stop server at end.
DATA FLOW
PYTHON FLOW

## Slide 11: Data Pipelines – Real-Time Implementation
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Muse EEG headband
Bluetooth
Mind Monitor app
Option 2:
OSC network protocol
python-osc
(Multi-threading server mapping message strings to handler functions)
pymongo/MongoDB (Capped Collection for immediate prediction)
DATA FLOW
PYTHON FLOW
Modified version for deployment
Prediction Model
(scikit-learn or keras)
Visual or audio feedback

## Slide 12: Data Wrangling - .csv file
3 experiment recordings were combined to form a dataset for modeling.
Without python control during recording, experimental conditions were marked manually in the Mind Monitor app.
Data was sorted into overlapping 2-second epochs, then mean and var of all numeric variables were computed as features.
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
5 = Eyes closed
4 = Body-scan
3 = Physical action
(Repeated button pressing)
2 = Mental action command
(Repeatedly willing something to happen)
1 = Baseline

## Slide 13: Data Wrangling – OSC Protocol
OSC messages included raw signal from EEG, accelerometer, gyroscope, and quality control flags.
10-second segments were rejected:
  if 5 or more flags were present.
  If the number of saved datapoints differed by more than 1.5%.
12 out of 60 segments were rejected.
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation

## Slide 14: Visualizations in Exploratory Data Analysis
Exploratory Data Analysis & Feature Engineering
Modeling
Real-Time Deployment
Curiosity & Hypothesis Generation
Self-Experimentation
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Time 
Frequency 
AMPLITUDE
AMPLITUDE
Time 
Frequency 
Time 
Frequency 
PHASE DIFF BETWEEN CHANNELS
COMPLEX MORLET WAVELET
Rely on visualizations to understand the brain’s non-linear dynamics.

## Slide 15: Univariate distributions
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation

## Slide 16: Complex Morlet Wavelets
A sine wave times a Gaussian, with Euler’s formula to expand into imaginary space.
A single convolution with a wavelet can compute:
  Band-pass signal
  Amplitude
  Power
  Phase (phase difference between channels is informative)
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Time 
Frequency 
AMPLITUDE
AMPLITUDE
Time 
Frequency 
Time 
Frequency 
PHASE DIFF BETWEEN CHANNELS

## Slide 17: Challenges of EEG signal
Highly non-linear dynamics make dimensionality reduction complicated.
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Unclear whether signal is more predictive when aggregated over a time segment (with mean & var), or if sequence information should be retained.
Given the small size of my early dataset (several hundred 2-second segments), I elected to aggregate.
I used a custom train-test process to separate the final 20% of each condition type from each of the 3 recordings as a test set.
Employed GridSearchCV with pipelines.
Time 
Frequency 
AMPLITUDE
AMPLITUDE
Time 
Frequency 

## Slide 18: Efficient modeling
Exploratory Data Analysis & Feature Engineering
Modeling
Real-Time Deployment
Curiosity & Hypothesis Generation
Self-Experimentation
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Favor model types with easily accessible feature importances.

## Slide 19: Cross-validation model search
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
2-second segments were fed into 12 scikit-learn pipelines:
StandardScaler()
{PCA, or no PCA}
{ One of six model types:
  # Support Vector Classifier
  # Linear Discriminant Analysis
  # Random Forest Classifier
  # AdaBoost Classifier
  # Gradient Boosting Classifier
  # Decision Tree Classifier}
Baseline (open eyes) vs Closed Eyes

## Slide 20: Consumer-Driven Discovery and Deployment
Exploratory Data Analysis & Feature Engineering
Modeling
Real-Time Deployment
Curiosity & Hypothesis Generation
Self-Experimentation
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation
Identify the most important subset of features.
Deploy a lightweight model.
The proximity to deployment lowers the opportunity cost of false positives.

## Slide 21: Recommendations
Important features appear to be power/amplitude throughout the tested frequency range of 2Hz-80Hz.
Variance in phase difference between channels appears to be structured.
  Phase diff is more stable within a brain hemisphere than across hemispheres.
  Phase shifts are known to reflect functional connectivity between brain regions.
  Cross-correlation analysis like Granger Causality may yield good results.
Wavelet convolution methods are effective.
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation

## Slide 22: Recommendations
Decision tree ensemble methods can be very effective in an unknown feature space.
Support vector classifiers may be best for well-understood feature spaces.
Parallel pipelines for binary classification may be more effective than a single multiclass predictor.
Consumer EEG interfaces like Muse may have undiscovered potential.
Automate experimentation for the benefit of consumers.
Problem Identification | Data Wrangling | Exploratory Data Analysis | Preprocessing | Modeling | Documentation